## Slide 1
SATCOM TRANSMIT BEAMFORMER
MATLAB Driver Quick Start Guide
2024 February 06

## Slide 2: overview
Renesas developed the F65xx Windows MATLAB driver to ease customer development and testing
This example requires the user to have a basic understanding of MATLAB programming, search path, and object oriented programming. Knowledge of the Instrument Control Toolbox is also recommended to automate test and measurement equipment.
Features:
  Supports only USB Interface Board (FTDI FT2232H USB-UART/FIFO IC) supplied by Renesas
  Developed as a MATLAB handle class to utilize object oriented features
  Supports register programming as well as bit-field (shared register fields) programming
  All I/O, bit shifting, and clocking is managed by driver

## Slide 3: Required HARDWARE
The Renesas Evaluation System contains of the following hardware required to use the MATLAB driver:
Renesas F65xx Evaluation Board
Renesas USB Interface Board
Power Supply Ribbon Cable
The F65XX MATLAB driver communicates with the device via the USB Interface Board. The F65xx EVB uses the following connections to interface with the USB Interface Board :
MOSI -> AD1
CLK -> AD0
CS -> AD3
MISO <- AD2
RESET -> AC0

## Slide 4: FTDI Windows Device Driver
The computer used to run this driver should first be used with the Evaluation System software. The supplied Evaluation Software should first be used to verify communication with the hardware.
The Evaluation Software installs a copy of the USB Interface Board driver if the computer is not able to connect to the internet.
The driver is available from FTDI at the following URL:
https://www.ftdichip.com/Drivers/CDM/CDM21228_Setup.zip
Please refer to FTDI Support website for any driver installation issues:
https://www.ftdichip.com/FTSupport.htm

## Slide 5: Required Files
The following file structure is provided in the distribution of the .zip file.
All files are required for the driver to function
All folders must be in the MATLAB search path
  F65xx_Examples
    F65xx_Sweep_Example.m
    F65xx_Array_Example.m
  DUT
    f65xx.m
    f65xx_enum_DEVICE_TYPE.m
    f65xx_enum_RF_LOAD.m
    f65xx_enum_SPI_MODE.m
    f65xx_enum_SUB_ARRAY_MODE.m
  FTDI
    FTD2XX_NET.dll
    FTD2XX_NET.XML
    ftdi_enum_BUS_NAME.m
    ftdi_enum_SPI_READ_MODE.m
    ftdiClass.m
    ftdiMpsseSpi.m

## Slide 6: MATLAB PATH
Please verify that your MATLAB path variable includes all of the folders supplied in the example.
The code will attempt to set the path for you with the line
addpath(genpath('c:\Renesas'));
If you install the code at a different location, this line of code must be changed and point MATLAB to the path where it is installed.
If you add the installation path and subfolders to your MATLAB path, you may comment this line or remove it.

## Slide 7: f65xx_Sweep_Example.m overview
To Communicate with a device, you must instantiate the driver class.
After the DUT object is created, you open communication with the USB interface board.
Set the SPI serial address
Define the type of device by autodetect or manually:
Program the device defaults
Load the software Gain Mapping Table
Load the device Fast Beam Steering SRAM
Enable the Master Bias (MB_EN_n field)
Disable Global Power Down (GLOBAL_PWD field)
Set the Gain Mapping Table index (1-128 index, array is 1 based)
Program the (VGA_SET _n field)
Program the (DR_SET_MSB_n field)
Program the (PS_SET_n field)
Set the active Fast Beam Steering Index
Close the connection to the USB Interface Board

## Slide 8: f65xx_Array_Example.m overview
To Communicate with a device, you must instantiate the driver classes.
After the DUT object is created, you open communication with the primary device to the USB interface board.
Open communication with the secondary devices. Pass in the primary DUT class.
Set the SPI serial addresses
Define type of device and apply to all devices
Program the device defaults
Load the software Gain Mapping Tables
Load the device Fast Beam Steering SRAMs
Enable the Master Bias (MB_EN field)
Disable Channel Power Downs ( channels 1-8) (CH_PWD_n field)
Disable Global Power Downs (GLOBAL_PWD field)
Set the active Fast Beam Steering Index
Set the Global Power Downs (GLOBAL_PWD field)
Close the connection to the USB Interface Board

## Slide 9
Appendix

## Slide 10: USB Interface board schematic

## Slide 11: modified factory Board test

## Slide 12
THANK YOU